## Slide 1: Transport Canada Update
May 4, 2015

## Slide 2
Agenda
Waiver
Background
  CSA 2001 and related regulations
  True North II sinking off Tobermory in 2000
Definitions
  Pleasure Craft, Sheltered waters, Near Coastal Class II
TC Regulation
  Construction, equipment, operator training for area of operation, registration
Examples
Transport Canada Update May 2015
Slide: 2

## Slide 3: CSA 2001 & related regulations, standards
Canada Shipping Act 2001
  Came into effect in 2007
    New or revised regulatory interpretations
Small Vessel Regulations
Vessel Certificates Regulations
Marine Personnel Regulations
Vessel Construction Regulations
Competency of Operators of Pleasure Craft Regulations
Standard for Recreational Boating Schools
Transport Canada Update May 2015

## Slide 4: True North II Spotlight
Sank off Tobermory in June 2000
Student overnight outing in a marine park
True North II used to transport students
Vessel sank with 20 aboard
2 Grade 7 students drowned
Vessel was
  Poorly maintained
  Modifications made it unsafe
  TC did not enforce regulations
  Did Operator meet “duty of care test”?
Civil Litigation Followed
Transport Canada Update May 2015

## Slide 5: Definitions
Pleasure Craft
Passenger
Sheltered waters
  Areas listed in the Vessel Certificates Regulations
    By areas with date ranges
  Non-tidal waters where you can never be more than 2.5 miles from shore
    (rivers, small lakes)
Transport Canada Update May 2015
“pleasure craft” means a vessel that is used for pleasure and does not carry passengers,
“passenger” means a person carried on a vessel by the owner or operator, other than the master, crew, guest, victim of shipwreck

## Slide 6: Definitions
Transport Canada Update May 2015
“near coastal voyage, Class 2” means a voyage
(a) that is not a sheltered waters voyage; and
(b) during which the vessel engaged on the voyage is always
(i) within 25 nautical miles from shore in waters contiguous to
Canada, the United States (except Hawaii) or
Saint Pierre and Miquelon, and
(ii) within 100 nautical miles from a place of refuge
Near Coastal Voyage, Class 2

## Slide 7: Transport Canada Regulation
Transport Canada Update May 2015
Regulations depend on
  vessel type
  vessel size
  vessel use
  Vessel Use is Key
  Determines whether the vessel is a pleasure craft or not
  Regulation is different of pleasure / non-pleasure craft
  Areas Impacted are construction, safety equipment and personnel training

## Slide 8: Transport Canada Regulation
Transport Canada Update May 2015
Vessels Less than 6 metres
Construction
Same requirements for vessels < 6 metres (19.5 feet)
Safety Equipment (Small Vessel Regulations)
Pleasure craft plus flares, first aid kit, fire extinguisher
Registration
Non pleasure craft must be registered
Cost $50, valid 5 years, may submit batches At present exemption for
human-powered vessels (such as canoes or kayaks)
sailing vessels less than 8.5 metres
small power-driven vessels - motors < 10 horsepower (7.5 kW)

## Slide 9: Transport Canada Regulation
Transport Canada Update May 2015
Personnel Training and Operation Areas
PCOC = Pleasure Craft Operator Card
up to 6 passengers,
8 metres,
sheltered waters
SVOP
SVOP = Small Vessel Operator Proficiency
up to 12 passengers,
5 Gross tons (8.5 metres),
Near Coastal Class II

## Slide 10: Transport Canada Regulation
Transport Canada Update May 2015
PCOC – written exam, may be internet based, takes about 4 hours
SVOP (for 2015) – 4 days classroom, written exam, must be 18, also requires 1 day Med A3
SVO certification (replaces SVOP in 2016) - 5 days classroom, written exam, Must have VHF ROCM and Marine First Aid

## Slide 11: Transport Canada Regulation
Transport Canada Update May 2015
Is it a Pleasure Craft?
Is the vessel used for pleasure purposes only
Is the operator paid for service or do the passengers pay – probably not pleasure craft

## Slide 12: Examples Pleasure Craft
Transport Canada Update May 2015
Yacht Clubs:
include vessels that are used for joint recreational activities.
all the people involved are using the vessel(s) for the pleasure of the group.
For yacht clubs, a joint recreational activity includes an activity that meets the following criteria:
  The vessel used is wholly owned by or on behalf of a members’ club or organization;
  The vessels are used only for the pleasure of members of that club/organization;
  Any charges levied are paid into club/organization funds and applied for the general use of the club/organization; and
  Members are co-owners of the club/organization

## Slide 13: Examples Pleasure Craft
Transport Canada Update May 2015
Yacht Clubs:
Example: A vessel owned by a yacht club and used for safety and life guarding at a recreational event.
Explanation: A club member is part owner of the vessel, and the vessel is being operated in support of the joint recreational activity of club members. There is no specific fee associated with this activity.

## Slide 14: Examples Pleasure Craft
Transport Canada Update May 2015
Example: A vessel owned by the operator is used to transport building materials as a favour to a friend. The friend pays for fuel and expenses.
Explanation: Even though there is an exchange of money, there is no object of profit and the vessel is still being used for the pleasure of the operator

## Slide 15: Examples Non-Pleasure Craft
Transport Canada Update May 2015
Example: A vessel is used to transport people from one point to another for a fee (such as a water taxi).
Explanation: The vessel is being used to provide a service (transportation).

## Slide 16: Examples Non-Pleasure Craft
Transport Canada Update May 2015
Example: A vessel owned by a yacht club and used to provide transportation or training to members or non-members for a fee.
Explanation: The vessel is not being used for a joint recreational activity. The fee is being paid directly for the service or training.

## Slide 17: Examples Non-Pleasure Craft
Transport Canada Update May 2015
Example: A vessel is used by an instructor to teach students how to safely operate the vessel for recreational purposes. The vessel is owned by the sailing instructor or a recreational boating school.
Explanation: The instructor is the person in charge of the vessel and is using the vessel as part of a business activity.

## Slide 18: Examples Non-Pleasure Craft
Transport Canada Update May 2015
Example: A vessel operated by an instructor at a summer camp who is employed to teach sailing techniques to campers. Fees are paid specifically for the training activity.
Explanation: The fee is being paid specifically for the training and is not paid toward the general cost of the camp

## Slide 19: Examples Non-Pleasure Craft
Transport Canada Update May 2015
Example: A vessel is used by an instructor to teach students how to safely operate the vessel for recreational purposes. The vessel is owned by the sailing instructor or a recreational boating school.
Explanation: The instructor is the person in charge of the vessel and is using the vessel as part of a business activity.

## Slide 20: Examples Non-Pleasure Craft
Transport Canada Update May 2015
Example: A vessel operated by a volunteer member of a not-for-profit organization to provide sightseeing opportunities free of charge.
Explanation: An organization has engaged a person to operate the vessel to provide a service – in this case, sight-seeing.

## Slide 21: Outstanding Issues
Transport Canada Update May 2015